## Slide 1
Architectures & deployment

## Slide 2
WiFi access point
UPS
Router
PcVue
Bay
Client stations
Server stations
Central version server station
FrontVue station
Firewall
Mobile devices
Web backend
HTML5
Proprietary archives
HDS archives
Web deployment console
IIS sever
Graphics
ContextVue
Notes: Not in the slideshow - For future copy/paste only

## Slide 3
Role | Definition
Data acquisition | Communication with field devices, Real time data and alarm production, Serves real time data and alarms to other stations
Historical data | Consume real time data and alarms produced by other stations, Handles data storage, the recording and replay of historical data, Manages connections to RDBMS, Serves historical data to other stations.
Web server | Consume real time data and alarms produced by other stations, Consume historical data produced by other stations, Manages the interface with IIS, Serves Web clients including WebVue clients, TouchVue clients, the WebScheduler and the Web Services Toolkit clients
Gateway | For the secure transfer of data between 2 networks Consume real time data, alarms and historical data produced by other stations on one network, Serves real time data, alarms and historical data to stations on another network
HMI | Display mimics, graphics, alarm viewer, log viewer, trend viewer... to the user
Building blocks

## Slide 4
Building blocks | Role | Typical deployment
Standalone station | -Data acquisition -Historical data -HMI -Does not have the capability to exchange data with other stations | -As a Desktop Application -Under a desktop OS
SCADA Station | -Data acquisition -Historical data -HMI | -As a Desktop Application if it requires an HMI -Under a desktop OS Or -As a Windows Service if an HMI is not required -Under a server OS
Data Acquisition Server | -Data acquisition -Historical data -HMI | -As a Windows Service -Under a server OS
Building blocks

## Slide 5
Building blocks | Role | Typical deployment
Client station | -HMI | As a Desktop Application Under a desktop OS Or with a server OS hosting Remote Desktop Services combined with lightweight terminals used as operator workstations
Historical Data Server | - Historical data | -As a Windows Service -Under a server OS
WEB Server | - IIS -Hosts the Supervisor's web services required to serve the web & mobile applications | -Requires Microsoft IIS -Under a server OS
WEB backend | - PcVue station acting as a gateway to provide data to the WEB server | -As a Windows Service -Under a server OS
Building blocks

## Slide 6
Building blocks | Role | Typical deployment
Mobiles clients | -Remote monitoring and control over the Internet or Intranet via desktop or mobile devices -WebVue clients and TouchVue clients or RDS clients | -Using a Web browser or a Web App On a desktop PC or a mobile device
Engineering station | -Depending on the architecture and project design, an engineering station can have very different roles, ranging from those of a data acquisition server (for testing communication with field devices), to archive server or just an HMI workstation (to design mimics). Project development and maintenance. Project and libraries version management. Interoperability with third-party generation tools. | -As a Desktop Application -Under a desktop OS
Building blocks

## Slide 7
IT Network
Devices
Data acquisition network
The simplest architecture
To monitor and control your process from a single “all-in-one” station
All performances of a PcVue station for a stand-alone architecture
Stand-alone station
Notes: Standalone stations are usually operator panels, it is the simplest architecture with all functions and roles integrated into a single station.
In a traditional single-user configuration, PcVue monitors and/or controls all devices on the industrial network and also handles user requests. PcVue can support some tens of thousands of variables on a single station.
The PcVue single station is an all-in-one standalone HMI station to monitor and control the process using the standard features of PcVue :
Data acquisition,
Real-time database,
HMI,
Archiving ,
Alarms and logs,
Trends,
Data processing , reporting
Users management
OPT : SQL Server or proprietary
OPT : Parler de report ?

## Slide 8
The simplest multi stations architecture
The process is monitored from several remote user stations
Data processing network load optimized
IT Network
Devices
Data acquisition network
PcVue
Clients
PcVue
Acquisition server
Multi-station
Notes: The simplest client/server architecture, for applications that require several user stations with a single connection to the industrial network.
The server is a data source (producer) that communicates with the devices and broadcasts data to the client (or consumer) stations. Communication among the PcVue stations works asynchronously and transmits the data in packets using the PcVue TCP/IP messaging.
The server station can be a full user station or a data acquisition server only. It performs all of the data processing for the application. The historical data can be on server side only, or local to each client station.
A client can connect to a server located in another geographical area via a connection using any media supporting TCP/IP with sufficient capacity including private telephone line, or even satellite link.
A usual variation is to separate Data Acquisition and Historical Data production on 2 different servers, or to have clients produce historical data locally.
MDT : Mal dit, ce ne sont pas les stations qui sont native TCP/IP
Archjvage sur le serveur et sur chaque client.

## Slide 9
To reduce the administration effort and costs
Low cost thin hardware clients
Installation free on thin clients
PcVue thin clients
Remote desktop server
PcVue client instances
PcVue historical data server
WiFi router
Devices
IT Network
Data acquisition network
PcVue Acquisition server
Multi-station with a Remote Desktop Server for deploying client stations
Notes: Windows Server, when configured with Remote Desktop Services, allows several users to concurrently use the resources of a single server and to execute applications installed on the server. A user interacts with applications using a thin client (also known as terminal) connected to the server using a network. The process of a user connected to Windows Server in this manner is called a Remote Desktop Session and uses a standard known as the Remote Desktop Protocol (RDP). Thin clients (including Wyse Thin Computing terminals under Linux or Unix) use RDP client software for managing the RDP.
In addition to running sessions using a remote desktop, Windows Server also runs a session using the local monitor, keyboard and mouse. This is referred to as the local session (or sometimes as a console session or interactive session).
When running the Supervisor on a RD Session Host server, an instance of the Supervisor can be run from each Remote Desktop Session and/or from the local session. Only a single copy of the Supervisor is installed.
This architecture, from a Supervisor's networking point of view is the same as the previous one except that as a way to rationalize the deployment of
client station, RDS and lightweight terminals are used.
In this example a PcVue Client is installed on a station with Windows Server operating as a Remote Desktop Server (RDS).
This station is a RD Session Host server and hosts PcVue client instances. Users can open a Remote Desktop Session from any thin client and run a PcVue client instance. An HTML5 interface on the server allows any thin client equipped with a HTML5-compliant Web browser to access the PcVue applications through a RDS instance.
The PcVue Server, when there is only one, can also reside on the RD Session Host server.
The RD Session Host server must be configured to host multiple Client instances for supporting the required number of simultaneous sessions. The thin clients do not require any specific installation, which facilitates on-site deployment of the application.

## Slide 10
Very high level of security and system/data availability
Secure Client-Server setup with dual networks
Several user stations
Data processing and field networks data load optimized
PcVue Clients
Association of redundant PcVue acquisition servers
PcVue Historical Data Servers
Devices
IT Network
Data acquisition network
High availability
Notes: When a higher availability and resilience are required, this architecture, more distributed, brings redundancy and roles separation.
It is similar to the multi-station architecture but with data acquisition server and historical data server separation and redundancy.
The inter-station network (LAN and/or WAN) can be duplicated, as can the field network. There are then two independent paths between any client station and the data sources. Each PcVue client station maintains two connections with each server station and will attempt to switch between servers only when both of these connections are inoperable.
On an Industrial Ethernet network, PcVue can manage both communication media redundancy and device-level redundancy.
Each station can archive the data to improve the historical data availability.
A usual variation is to also include a Web Server and Web clients, thus combining permanent operator's seats and one-off user connections.

## Slide 11
S1
S3
S2
PcVue
Clients
IT network
PcVue
Acquisition server
Devices
Data acquisition networks
Devices
Devices
Distributed architecture
PcVue
Acquisition server
PcVue
Acquisition server

## Slide 12
Devices
PcVue
Clients
S1
S3
S2
S4
PcVue
Clients
PcVue
Clients
PcVue
Acquisition server
Process #1
Process #2
Process #3
PcVue
Acquisition server
PcVue
Acquisition server
IT Network
Passive PcVue mutualized server
  Association #1
  Association #2
  Association #3
Data acquisition network
Data acquisition networks
Mutualized servers
Notes: The mutualized architecture is an interesting variation of the high-availability.
When you have to monitor and control multiple processes, production lines, plants, buildings, sites... and can benefit from a reliable network, you can set up a high-end server that will be used as the standby server for multiple other zones. By mutualizing the standby server, you achieve redundancy and availability while minimizing the overhead of deploying and maintaining a fully duplicated set of servers.

## Slide 13
For very large scale applications and geographically widely distributed system
Several levels of control
Very flexible
PcVue Clients level II
Level I - Local sites
Level II – The operation center
PcVue
Clients level I
PcVue
Historical data
server
Field devices
PcVue Gateway Servers
WAN
Data processing network
PcVue TCP/IP messaging
Data acquisition networks
OPC
Level III – The dispatch center
Data processing network – PcVue TCP/IP messaging
Association of redundant PcVue acquisition servers
Association of redundant PcVue acquisition servers
Association of redundant PcVue acquisition servers
Multi levels implementation #1
PcVue
acquisition
server
Notes: When network segmentation is a concern, a gateway can be added to the architecture.
Such an architecture is useful when, for example, the system spans over a Wide Area Network, or when data consumers (client stations or data repository) are located in a less-trusted network.
Such a gateway can be deployed in a DMZ, and if necessary gateways can be redundant.
In a distributed architecture each station may be a data source (producer) for some variables and a consumer for some others. Moreover, some stations may act as data concentrators for a central control room located in another geographical area.
PcVue allows the development and deployment of multi-server/multi-client applications whereby the various server associations are configured to allow some of them to primarily retrieve information from devices, and others from other servers (as client stations do).
Central servers collect only a subset of all the information, allowing efficient monitoring of the devices from the central control room.
The level I – Local sites is composed of PcVue stations widely distributed getting the data from the field devices and making the data available to the level II through a Wide Aera Network with satellite connection for example.
The Level II – The operation center is the core of the architecture with redundant associations of PcVue servers to centralize the data from different stations from level I. Each association of server handles thousands of real time variables and archives the higher critical variable locally.
A pair of servers can also be dedicated to archive the low critical data to a DBMS.
The Client stations connected to the server stations are used as operation and engineering consoles and help the operators to monitor and control the variables from any sites (Real time, alarms…).
The level III – The dispatch center is the highest level of the architecture. It receives the main data unified from the level II through an OPC connection.

## Slide 14
For geographically widely distributed system
Several levels of control
For very large amount of data/high growth rate projects
Very flexible
FrontVue Clients level II
Level I - Local sites
Level II – The operation center
PcVue
Clients level I
PcVue
Historical data
server
Field devices
WAN
Data processing network
PcVue TCP/IP messaging
Data acquisition networks
OPC
Level III – The dispatch center
Field devices
Data processing network - OPC
OPC
Association of redundant PcVue acquisition servers
Data processing network – PcVue TCP/IP messaging
Association of redundant PcVue acquisition servers
Association of redundant PcVue acquisition servers
PcVue Gateway Servers
PcVue
acquisition
server
Multi-levels implementation #2
Notes: When the application becomes bigger (over 300 000 variables), it makes sense to optimize the architecture replacing the rich PcVue clients with the lighter FrontVue HMI clients to insure the scalability of the system.
FrontVue is a very lightweight OPC-based HMI client with no embedded treatment or archives. Connected to PcVue as an OPC client, it gets and allows monitoring and controlling real time data and can display alarms and historical data that are managed on PcVue side.
FrontVue refreshes only the data displayed which allows to:
minimize application start-up time on clients
dramatically reduce the data load on the network
FrontVue can connect on several OPC servers which allows to
connect to remote local servers for retrieving detailed information from any specific device.
display concatenated events from several PcVue servers to present a single/unique list to the operator in the alarms/logs viewers.

## Slide 15
Unique source of configuration
PcVue configuration elements generated from custom assets models
For very large projects with several engineering teams working concurrently
Custom assets integration
Centralized database
Custom assets models
Assets configuration
tool
PcVue Engineering station
Assets models
Others app
PcVue
Data Acquisition servers
PcVue
Archive server
PcVue
Client stations
PcVue configuration generation/synchronization
- Real-time Database - Processing - Connectivity
- Archives
- Graphics
Application Architect: PcVue modeling component
Smart Generator: PcVue 3rd party configuration import
Engineering team #1
Engineering team #x
Assets models import
Xml, Excel, DBMS,…
Notes: In very large projects many systems might be involved yet using the same assets models.
Several teams may need to work on separated part of the same project. The architecture presented here shows an example where configuration of assets models are done by a specific tool and are stored in a central database. Each team can work on specific assets and feed the same database.
PcVue can import the assets models directly from an assets configuration tool and/or from a centralized database and generate PcVue configuration elements including:
Real-time database,
Behaviors and data processing,
Connectivity
Archives
PcVue comes with several Smart Generators which can import 3rd party configuration from various sources: xml files, databases, PLC’s configuration platforms, CAD platforms,…
PcVue project can be generated/synchronized using the modeling tool Application Architect.

## Slide 16
Easy maintenance and deployment of a project and/or libraries
Unlimited number of versions
Modifications tracking
Reduce the risk of errors and loss
Devices
PcVue
Clients
PcVue
Engineering station
Association of redundant PcVue acquisition servers
Data acquisition networks
Data processing network – PcVue TCP/IP messaging
Engineering station with version management
Notes: To make the maintenance and the deployment of a project easier and faster, PcVue is delivered with a built-in central project management tool.
Different versions of a project and/or libraries are centralized in a shared directory on the network. They can be loaded and modified from any station on the network.
Usually a dedicated PcVue engineering station is used to host the central versions directory and to make the change for a project.
Any station can load and run manually any type of version, or automatically one reference version of a project and/or libraries from the central project directory.
The features supported are:
3 types of versions : development, operational and reference
Configurable content of a version
Track modification for each version
Automatic version numbering system
Unlimited number of versions (vs media free space)

## Slide 17
Web & mobile architectures
#1 All in one (not recommended)
Industrial network
PcVue
Backend/WEB IIS/Server
WEB console
Router
Field network
PcVue
Acquisition server
PcVue
Clients
Office network/Internet
PcVue backend and WEB/IIS servers hosted and run on the same computer
Non isolated networks
Low security level
Intended when the network is private and fully isolated from outside access
WebVue/TouchVue/SnapVue
Web & mobiles clients
WebVue/TouchVue/SnapVue
Web & mobiles clients
Notes: In this deployment scenario the PcVue Web Backend Station and the PcVue Web Server
Components are not separated and hosted and run on the same computer.
The Web/Mobile Client Systems are connected to the same logical network as the PcVue
Web Server Components.
When to use?
This architecture is intended for simple deployment scenarios with the Web/Mobile Client
Systems on the same logical network as the PcVue Web Backend Station.
Usage of this deployment scenario is considerable when the network is private and fully
isolated from outside access.
When not to use?
Do not use this deployment strategy when the network is open to incoming requests from
outside networks or open for unprotected access from unknown devices.
In particular, do not use this deployment strategy when access from web and mobile client
systems on the Internet is required and no further means of network security (such as VPNtunneling
for instance) are available.
Requirements
1. A local area network (LAN) to connect the Web/Mobile Clients to the Web Server
Station and to connect the PcVue Web Backend Station with the rest of the industrial
automation network (i.e. other PcVue data acquisition station or field level devices).
2. Clients on this network are supposed to trust the Web Server machine without
reservation, as they are on the same and, by definition, private network.
3. This architecture works with minimum requirements towards the trustworthiness of
the web server certificate.
A certificate from a certificate authority is not mandatory to proof the identity of the
Web Server Station.
4. This architecture can be deployed with a minimum level of network expertise.
Benefits
1. PcVue Web Backend station does not require more than one network interface card.
2. Works out of the box with no limitations, when using the IP address of the Web Server
computer to connect web and mobile clients.
3. Works well without DNS name resolution on Windows platforms. The Web Server
computer may be addressed by its hostname from Windows based web clients.
When using non-Windows based systems as web and mobile client systems, the
activation of the DNS-Server role on the Windows Server operating system of the
PcVue Web Backend station or the usage of a 3rd party DNS server on the Windows
client operating system of the PcVue Web Backend station can be a solution.
4. Can work without a Windows Server operating system on the PcVue Web Server
computer, even if the usage of a server operating system is highly advisable.
With hosting the PcVue Web Mobile Components on a Windows client operating
system certain limitations are to be expected, particularly in regard to the maximum
amount of incoming client connections.

## Slide 18
Web & mobile architectures
#2 Secured by isolation network and DMZ (recommended)
Industrial network
Field network
PcVue
Acquisition
server
PcVue
Client/Web Backend
Router
WebVue/TouchVue/SnapVue
Web & mobiles clients
Network office/internet/WAN
DMZ
WEB IIS server
WEB Console
PcVue backend and WEB/IIS are not on the same network
Isolated network
High level of security
WebVue/TouchVue/SnapVue
Web & mobiles clients
Notes: Description
In this deployment scenario the PcVue Web Backend station and the Web/Mobile Client
Systems are on different logical networks, at which these networks are segregated by a DMZ.
The inner network (LAN side of the DMZ) is seen as a private network. The outer network
(WAN side of the DMZ) is a less trusted network and typically an office network or the
internet.
The PcVue Web Server Components are hosted on a computer inside the DMZ.
This architecture provides optimized integration into IT networks and allows for maximum
compliance with IT guidelines and practices.
Level
When to use?
Usage of this deployment architecture is recommended wherever the Web/Mobile Clients are
outside of the industrial automation network.
This scenario allows for maximum secure deployment, in line with IT network segregation
practices, making sure that there are no undesirable incoming connection requests from
outside networks into the industrial automation network, including traffic monitoring at
network perimeters.
Requirements
1. The network infrastructure to segregate the private network from the lesser protected
network.
This includes a router and at least one firewall.
Both common DMZ architectures are supported, including single firewall setup and
dual firewall setup:
2. Support of the end user’s IT department is likely to be required, to properly set up
network segregation and name resolution.
This includes the proper configuration of:
- DNS
- Active Directory
- Routing
- Port Forwarding
3. In order to validate the identity of the Web Server computer on the lesser trusted
network and to prevent Man-in-the-Middle attacks, usage of a fully trusted certificate
is a must.
- This certificate can be issued by the IT department with their office network Active
Directory server.
- This certificate can be issued by the IT department with a trusted CA, if accessed
from external Web/Mobile Clients (Internet access).
- This certificate may be issued with the help of the Let’s Encrypt wizard of the WDC.
4. A DNS server is required on the lesser trusted network.
5. A Windows Server operating system on the Web Server computer, and ideally also on
the PcVue Web Backend Station.
6. The PcVue Web Backend Station must be accessible from the Web Server computer at
least by its IP address. Access via hostname is also possible, given that a mean of
name resolution is present from within the DMZ:
- A dedicated entry in the hosts file of the Web Server computer.
- A DNS server within the Industrial Automation network that is accessible from the
DMZ.
If not already available, the activation of the DNS-Server role on the Windows Server
operating system of the PcVue Web Backend Station can be a solution.
Note: Allowing access from a computer within a DMZ into the private network
contradicts with DMZ common patterns and practices. For technical reason however,
TCP port 8090 needs to be opened into that direction.
7. The level of network and IT expertise required to deploy this architecture is
intermediate to high.
Benefits
1. This architecture allows for convenient access from Internet or Intranet Web/Mobile
Clients, by exposing the web and mobile services and applications of the Web Server
Station under a FQDN.

## Slide 19
Web & mobile architectures
#3 Simplified NAT
Industrial network
Field network
PcVue
Acquisition server
WEB IIS server
WEB Console
Perimeter security device
Router/Firewall/VPN
Organization-owned
Network office/internet/WAN
Set-top box
ISP-owned
Remote access to small-scale systems
Intended when no managed IT infrastructure is available.
WebVue/TouchVue/SnapVue
Web & mobiles clients
WebVue/TouchVue/SnapVue
Web & mobiles clients
Notes: Description
This deployment scenario corresponds to a single private LAN, the Industrial network, where both the Web Server, the PcVue Web back end station and most Web & Mobile clients reside. A dedicated Internet access is used for remote connections.
In this deployment scenario the Web & Mobile clients are distributed across both sides of a NAT boundary (local and remote web clients).
Although it is technically feasible to deploy this architecture as is, it is not recommended to do so without the deployment of further security measures.
The list of potential measure includes usage of a VPN and client address locking, in which case the architecture may be logically equal to Architecture #1. By using the network perimeter’s dedicated DMZ port for establishing a dedicated network segment, in which case the architecture is a simplified version of Architecture #2. In any case, it is recommended to separate the PcVue Web back end station and the Web Server as described in Architecture #2, which by itself is an additional security measure.
If the Internet access is provided via a 3rd party and requires a device such as a set-top-box supplied and operated by the ISP, it is strongly recommended to install an appliance designed to control the network perimeter. In particular, it is recommended to refrain from alternative solutions, such as the “Exposed Host” pattern.

## Slide 20
Field network
Server station
ContextVue
Server
SnapVue Clients
Contextual engine- ContextVue server
Standalone
  1 data acquisition driver
  Contextual services & features
Connected to PcVue
  No direct communication with equipements
  Get the data from a PcVue station via Winnet
Connected to a 3rd party system
  No direct communication with equipements
  Get the data from a 3rd party system via OPC
LAN/WAN
PcVue
Other systems
OPC
WINNET
SnapVue
Deployment options
Notes: Standalone: « Starter kit »
  1 data acquisition driver
  Contextual services & features
Connected to PcVue: « Professional edition »
  No direct communication with equipements
  Get the data from a PcVue station via Winnet
Connected to a 3rd party system: « Enterprise edition »

## Slide 21
To reduce the number of physical stations
To reduce the administration effort and cost
Low-cost thin clients
Installation free on thin clients
Comply with IT requirements
    Application virtualization
The host computer can run different versions of PcVue or FrontVue in isolated environments
Setting up a working environment for one-off operations becomes easy
Setting up an ancient operating system is possible
Runs under Windows 7, Windows 8, Windows 8.1, Windows 2008 SP2 and 2008 R2 SP1,2012 and 2012 R2 Server and VMWare
        2.Ressources virtualization
Virtualized environments can run various PcVue servers under different operating systems on a single physical machine
PcVue licenses can be of different types
Dynamic assignment of virtual machines to physical hosts according to resources optimization rules
Virtualisation
Notes: Virtualization, in computing, refers to the act of creating a virtual (rather than actual) version of something, including but not limited to a virtual computer hardware platform, operating system (OS), storage device, or computer network resources.
Hardware virtualization or platform virtualization refers to the creation of a virtual machine that acts like a real computer with an operating system. Software executed on these virtual machines is separated from the underlying hardware resources.
In hardware virtualization, the host machine is the actual machine on which the virtualization takes place, and the guest machine is the virtual machine. The words host and guest are used to distinguish the software that runs on the physical machine from the software that runs on the virtual machine.
Virtualization of industrial applications can benefit many departments involved: IT, Engineering and operations.
Source : Wikipédia

## Slide 23
Position